## Slide 1: LIGHT DESIGN
Technical Theatre

## Slide 2: LIGHT DESIGN
Purpose of Light Design:
to engage the audience through the use of
Color
Texture
Mood
Energy
Cell Block Tango” – Chicago
http://youtu.be/KA6R1DMb-Z8
Light directs an audience’s FOCUS
Lights allow the actors, action and artistic elements to be seen
Used for more than practical lighting.
Est. setting and mood
Est. emotional energy of characters

## Slide 3: ESSENTIAL QUESTIONS
What precautions are necessary to insure the safety of the performers?
How do the elements of Lighting Design work together to realize the director’s vision?

## Slide 4: LIGHT DESIGN
FUNCTIONS OF STAGE LIGHT
Visibility: light so aud can see actors, set, props, etc.
Selective Focus: directing aud’s attention to look at a specific area/character on stage
Modeling: using texture to emphasize the highlight or shadows of things, as to make “it” look real
Mood: use of color to determine time of day or to emphasize emotional context of script/characters
Style: realistic vs. nonrealistic
Information: est. location, time, space

## Slide 5: SELECTIVE FOCUS
As the cops found Susie in the corner of the room, she stood up showing her hands, each bloody from the stabbing.
The cops shine their flashlights on her hands to help focus the audiences’ attention there.
Wait Until Dark

## Slide 6: MODELING
Using a stick gobo pattern to resemble the feel of hay/straw in the field.

## Slide 7: MODELING, MOOD, STYLE
MODELING : using shadow to purposely emphasize the hidden desires and the frightening freaks
MOOD: over stimulating with colored light, multiple light sources, multiple gobo patterns
STYLE : non-realistic; green light, chaotic patterns
The Elephant Man

## Slide 8: LIGHT DESIGN
CONTROLABLE QUALTIES OF LIGHT
Distribution: direction of light (light source), size, shape, quality
Intensity: level of brightness
Movement: timed cues, onstage/offstage lights; practicals, light source
Color: determined by gel color & intensity

## Slide 9: PRACTICALS
The use of practicals in this set gives this murder mystery the ominous feel it needs, plus establishes the very real interior set these character will occupy, as they turn lights on and off lights upon entering and exiting.
The Mousetrap

## Slide 10: COLOR
A dim fuchsia gel color on the Siamese twins, gives these girls the eerie feel the director was looking for as they stood there looking out at the audience in their freak show cage.
The Elephant Man

## Slide 11: LIGHT SAFETY
Keep equipment in good working order
No food or drink near light board
Use dust cover on light board
Never touch the lamp with fingers
Always wear gloves when focusing
Wear closed toed, rubber shoes
Report wet or damp conditions
Know where the fire extinguishers are

## Slide 12: LIGHT FIXTURES
ELLIPSOIDAL REFLECTOR SPOTLIGHT (ERS)
Sizes: 6 x 9, 6 x 12, 6 x 16 (6=lens; 9/12/16 =focal pt)
Focused light
Best for front light
Throw = long distances
650W - 1000W
(2) Plano-convex lens = )(
bench focusing on back
Use shutters for added focusing
Used for “specials”

## Slide 13: LIGHT FIXTURES
SOURCE FOUR
SIZES: 5’, 10’, 14’, 19’, 26’, 36’, 50’, 70
Directional spotlight
THROW: long and short distance
LAMP: 375-750 watts
575 watt HPL equal to a 1000w lamp yet outperforms the length
FOCUSING: lamp focus, rotating barrel & shutter
OTHER: Gobo and Accessories Slots
Cast Aluminum Construction with bulb in back of fixture = heat escapes out the back = SAFER

## Slide 14: The Diviners – unfocused “specials”

## Slide 15: SPECIALS
General Lighting was used in this show, however, at the end, the lights slowly faded out except for one SPECIAL that was left on the two here. The final moment of the play just before she dies in his arms.
The House of Blue Leaves

## Slide 16: LIGHT FIXTURES
FRESNEL
Sizes: 6”, 10”, 12”
= (diameter of lens)
Soft Light (general)
Best for front (fill light) and back light
Throw = short distance only

## Slide 17: LIGHT FIXTURES
SCOOP
SIZE: 10” 14” 16” 18”
PURPOSE: multi-purpose reflector floodlight
Used in theatre and TV as a flood light where space limitation is a factor.
Ideal for set hallways and window backings where color blending and smooth even washes of light are required.
PAR CAN
Fill light – best for “filling” a space with light
Non directional
Can be gelled

## Slide 18: LIGHT FIXTURES
INTELLIGENT LIGHTING
(automated lighting, moving lights, moving heads)
Lights that are automated or have mechanical abilities
“Intelligence” really lies with the programmer/operator of the show rather than the instruments
http://youtu.be/yCByNEigEJM
http://youtu.be/TLOFI-uII3w

## Slide 19: LIGHT FIXTURES
STRIP LIGHT
3 or 5 circuit lights which projects different colors individually or together
Stationary or hung
LED STRIPS
Cyc wash with 144 calibrated red, green, blue, white and amber LEDs
Covers long throws smoothly and evenly.

## Slide 20: The Diviners – LED Cyc Lights

## Slide 21: LIGHT FIXTURES
FOLLOW SPOT
Used where manual control of an intense lighting beam is required to “follow” a performer
Vary beam size, quality, and color
Used a lot in musicals to “follow” the lead singer

## Slide 22: LIGHT ACCESSORIES
GOBO
GOBO
HOLDER
COLOR GEL
GEL FRAME

## Slide 23: The Diviners – Cloud Gobo

## Slide 24: LIGHT ACCESSORIES
GOBO ROTATOR
WATER GOBO
GLASS GOBO

## Slide 25: The Diviners – Lightening Gobo & Water Gobo Rotator

## Slide 26: LIGHT ACCESSORIES
TOP HAT
IRIS
BARN DOORS

## Slide 27: LIGHT PLUGS
EDISON
TWIST LOCK
STAGE PIN
TWO-FER

## Slide 28: LIGHT MAINTENANCE
Never run lights at 100%
Running lights at 80% extends life by 2000 hrs
Never touch lamp
Clean lens and glass with rubbing alcohol
Clean shutters with steel wool and graphite powder

## Slide 29: LIGHT DESIGN THEORY
“THE MCCANDLESS SYSTEM”
Stanley McCandless “system” of covering a stage with general light.
Does not address specials
Only uses key light
Fill light is added afterwards to fill in shadows or dark area.

## Slide 30: LIGHT DESIGN THEORY “THE MCCANDLESS SYSTEM”
Each acting area is lit by two lights, each from a position 45 degrees above and to from the center of that area (front lights).
Why? to place feature enhancing shadows on the actor and to draw the actor away from the background.
Ellipsoidals are ideal for front lighting.

## Slide 31: LIGHT DESIGN THEORY
“THE MCCANDLESS SYSTEM”
Example of Front light
Don’t Drink The Water
Leading Ladies

## Slide 32: LIGHT DESIGN THEORY “THE MCCANDLESS SYSTEM”
To separate the actor from the background and provide a 3-dimensional appearance, down lighting and backlighting are important.
Unless trying to achieve a special effect, this type of lighting is not as bright as the front lighting.
Fresnels or PAR cans are ideal to use for backlighting.

## Slide 33: LIGHT DESIGN THEORY
“THE MCCANDLESS SYSTEM”
Example of Backlight
A Little Night Music
Wait Until Dark

## Slide 34: LIGHT DESIGN THEORY
USING COLOR
warm: bastard amber;
neutral: surprise pink;
cool: pale blue

## Slide 35: LIGHT PLOT areas 1-2-3

## Slide 36: LIGHT PLOT areas 4-5-6

## Slide 37: LIGHT PLOT areas 7-8-9

## Slide 38: LIGHT PLOT all areas

## Slide 39: LIGHT FIXTURE SYMBOLS

## Slide 40: LIGHT PLOT EXAMPLE

## Slide 41: LIGHT PLOT- the elephant man

## Slide 42: The elephant man
Although its missing some information, what is there, corresponds with the light fixtures on the light plot.
This sheet allows space for specific details about each light, where there is not room on the light plot.

## Slide 43: INSTRUMENT SCHEDULE
A detail list of light fixtures noting where they hang, what area they light and special notes:
  Gel colors
  accessories
Should correspond with the light plot
Instr.#-------- Circuit# | Instrument | Batten | Area | Gel Color | Accessories/notes
1-1 | S4-19 | A | IV | R01 | iris
2-2 | Fr 10” | A | X | R27 | Shutter DR
3-3 | S4-50 | B | XI | R52 | none

## Slide 44: LIGHT PRODUCTION
LIGHT DESIGNER
  Light Research
  Light Notes
MASTER ELECTRICIAN
  Light Plot
  Instrument Schedule
LIGHT CREW
  Hang lights off plot & I.S.
BOARD OPERATOR
  Light cue sheet
Wicked - Lighting
http://youtu.be/QUKDU3r6MYY
Billy Elliot – “Lights the Lights”
http://youtu.be/spG3J4ODJSQ
Spiderman-Light Design
http://youtu.be/k4FinZS274I